## Slide 1
Smart Laboratory
Safety System
Using ESP32, Firebase Realtime Database & MIT App Inventor
NAME
Chitturi Sanjay Kumar
ROLL NO.
24B11EC057
DEPT.
Electronics & Communication Engg.
UNIVERSITY
Aditya University
IEEE SPS STUDENT BRANCH
Notes: Title slide. Introduce yourself and the project. This is an IoT-based lab safety project built during your internship.

## Slide 2
AGENDA
What We'll Cover
01
Project Overview
Motivation & objectives
02
System Architecture
Three-tier IoT design
03
Hardware Components
ESP32, sensors & actuators
04
Software Implementation
Firmware, Firebase & mobile app
05
Results & Testing
Scenario validation & metrics
06
Conclusion
Summary & future work
Notes: Walk through the agenda. Six main sections: overview, architecture, hardware, software, results, conclusion.

## Slide 3
01
Project Overview
THE PROBLEM
✗ Laboratories contain hazardous chemicals, fire risks & high-voltage equipment
✗ Traditional safety relies on manual inspection — not real-time
✗ No instant alert system for remote stakeholders
✗ Unauthorized access goes undetected
✗ No centralized data logging or historical analysis
THE SOLUTION
✓ ESP32-based multi-sensor IoT node for continuous monitoring
✓ Real-time threshold detection with auto alarm & relay
✓ Firebase cloud sync for instant remote visibility
✓ PIR motion sensor for unauthorized access detection
✓ Android app with color-coded Safe / Danger alerts
Notes: Explain the core problem: labs are dangerous and conventional safety is reactive, not proactive. Our solution is always-on IoT monitoring.

## Slide 4
02
System Architecture
TIER 1
Sensing &
Actuation Layer
▸ DHT22 – Temp & Humidity
▸ MQ-2 – Gas Detection
▸ PIR – Motion Sensor
▸ Fire Sensor (KY-026)
▸ Relay / Buzzer / LED
TIER 2
Processing &
Communication Layer
▸ ESP32 Dual-core MCU
▸ Threshold evaluation logic
▸ GPIO control for actuators
▸ Wi-Fi / HTTPS upload
▸ Firebase ESP Client lib
TIER 3
Application
Layer
▸ Firebase Realtime DB
▸ Authenticated access
▸ NoSQL JSON structure
▸ MIT App Inventor app
▸ Color-coded alerts
▶
▶
Wi-Fi / HTTPS / Firebase SDK
Notes: The system uses a 3-tier architecture: sensors feed into ESP32, which pushes data to Firebase, which the Android app reads in real time.

## Slide 5
03
Hardware Components
●
ESP32 Dev Module
Core microcontroller with dual-core CPU, Wi-Fi & BT
●
DHT22 Sensor
Temperature (±0.5°C) & humidity (±2% RH) — GPIO 27
●
MQ-2 Gas Sensor
Detects LPG, methane, CO & smoke — Analog GPIO 35
●
PIR (HC-SR501)
Motion detection 7m range 120° FOV — GPIO 15
●
Relay Module
Controls mains-powered exhaust / ventilation — GPIO 2
●
Buzzer + LED
Audible & visual alarm inside lab — GPIO 14 / 13
Notes: Explain each component briefly. Highlight that ESP32 replaces NodeMCU with better specs — dual core, more GPIO, native Wi-Fi.

## Slide 6
03
Pin Configuration & Safety Thresholds
Component | ESP32 GPIO | Signal Type
DHT22 | GPIO 27 | Digital (1-Wire)
PIR Sensor | GPIO 15 | Digital Input
Fire Button | GPIO 4 | Digital Input
MQ-2 | GPIO 35 | Analogue (ADC)
Relay | GPIO 2 | Digital Output
Buzzer | GPIO 14 | Digital Output (PWM)
LED | GPIO 13 | Digital Output
Component GPIO Signal Type
⚠ DANGER THRESHOLDS
Temperature
> 50 °C
Gas (MQ-2 ADC)
> 3800 counts
Motion (PIR)
Any detection
Fire Sensor
Triggered
Any ONE condition → DANGER state
Notes: ESP32 GPIO assignments. Thresholds are hardcoded in firmware — any single threshold exceeded triggers the full alarm.

## Slide 7
04
Firmware – ESP32 Control Loop
// Simplified main loop (runs every 1 second)
float temp = dht.getTemperature();
int gas = analogRead(MQ2_PIN);
int mot = digitalRead(PIR_PIN);
int fire = digitalRead(FIRE_PIN);
bool danger = (temp > 50.0) ||
(gas > 3800) ||
(mot == HIGH) || (fire == LOW);
digitalWrite(RELAY_PIN, danger ? HIGH : LOW);
digitalWrite(BUZZER_PIN,danger ? HIGH : LOW);
Firebase.RTDB.setFloat(&fbdo, "/Lab/temp", temp);
Firebase.RTDB.setString(&fbdo, "/Lab/status",
danger ? "Danger" : "Safe");
1
Read Sensors
DHT22, MQ-2, PIR & Fire — every 1 second
2
Evaluate Safety
OR-logic: any threshold breach = Danger
3
Actuate Locally
Relay, Buzzer & LED respond immediately
4
Push to Firebase
Upload JSON to /Laboratory node via HTTPS
Notes: Walk through the 4-step control loop. Emphasize OR-logic: even one hazard triggers the full response. Local actuation is instant; cloud is async.

## Slide 8
04
Firebase & Mobile Application
🔥 Firebase Realtime Database
{ "Laboratory": {
"temperature" : 24.5,
"humidity" : 42.0,
"gas" : 1230,
"motion" : 0,
"fire" : 0,
"relay" : 0,
"status" : "Safe"
}
}
🔒 Security Rules: Read/Write restricted to authenticated users only
📱 MIT App Inventor App
🔑 Login Screen
Firebase email/password auth
📊 Live Dashboard
All sensor values updated in real-time
🟢 Safe Indicator
Green badge — all within limits
🔴 Danger Alert
Red badge — immediate notification
🔄 Auto Refresh
FirebaseDB GotValue event listener
Notes: Firebase stores a single /Laboratory JSON node. The app listens via ValueEventListener — no polling, instant push. Auth prevents unauthorized reads.

## Slide 9
05
Results & Testing
1 s
Sensor Sampling
Interval
<500ms
Firebase Upload
Latency
<800ms
App UI Refresh
Latency
<1.5 s
End-to-End Alert
Latency
Scenario Testing
► Normal Operation
✓ All safe, relay OFF, green app indicator
► Gas Leak (MQ-2 > 3800)
✓ Immediate Danger, relay + buzzer + red alert
► Temperature > 50°C
✓ Danger state, all actuators triggered
► Motion Detected (PIR)
✓ Unauthorized access alert activated
Validated using Wokwi Simulator + Firebase Console
Notes: All 4 scenarios passed. Highlight the sub-1.5-second end-to-end latency — this is well within human reaction time, so it's safe enough.

## Slide 10
06
Conclusion & Future Work
✅ What We Achieved
✓ Multi-parameter IoT lab safety monitoring
✓ Sub-1.5 s end-to-end hazard alert latency
✓ Autonomous local response (relay & buzzer)
✓ Firebase cloud sync with authenticated access
✓ Android app with real-time color-coded alerts
✓ Validated on Wokwi + Firebase Console
🚀 Future Enhancements
→ Replace push-button with KY-026 flame sensor
→ SMS/Email alerts via Twilio / SendGrid
→ Historical data analytics & trend charts
→ MQTT for lower-latency communication
→ Offline buffering via ESP32 NVS storage
→ Edge AI anomaly detection (TinyML)
Notes: Summarize: the system works, meets all objectives, validated through simulation. Future: real sensors, TinyML at the edge, MQTT.

## Slide 11
Thank You
Questions & Discussion
Chitturi Sanjay Kumar
Roll No. 24B11EC057
B.Tech Electronics & Communication Engineering
Aditya University
IEEE SPS Student Branch Chapter
Notes: Wrap up. Invite questions. Emphasize this is both an internship major project and a potential IEEE conference submission.